## Slide 1: PSL overview

## Slide 2: Formal Specifications
Properties and specifications defined in natural languages are imprecise, long and hard to understand, …
  What does this mean: “every request must remain asserted until a grant is received unless the request is canceled first?”
  Which signals are meant? What does “until” mean? …
Property Specification Language (PSL) provides a way to formally specify assertions in a compact and precise way

## Slide 3: PSL – The language for Assertions
Property Specification Language (PSL) is based on the Sugar language from IBM
PSL has been selected by Accellera as the basis for its standard property specification language
PSL endorsement and adoption is growing rapidly…
“A Vendor-neutral standard that’s open to anyone to use and/or build tools around so customers are not locked to a single vendor”

## Slide 4: PSL is a layered language
Boolean layer
  Boolean expressions involving HDL, logic operators and PSL functions. It is evaluated immediately, at an instant in time. a) (ack) (namely, ack == 1) b) (out == prev(in, 1))
Temporal layer
  Sequential expressions and properties, both of which descrive behavior of the design over time through temporal operators. a) {s1;s2;s3} b) always (req -> next[1](!ack))
Boolean
Temporal
Verification
Modeling

## Slide 5: PSL is a layered language
Verification layer
  Directives for the verification tool that specify what to do with the defined sequences and properties a) assert (p) b) cover (s)
Modelling layer
  Directives to declare and give a behavior to design’s inputs, auxiliar symbols/variables (useful to formal verification tools in which the behavior of such elements isn’t otherwise specified)
Boolean
Temporal
Verification
Modeling

## Slide 6: Example
  logic (1:5) a;
  P1: assert always ( req -> next[2] (out < a) ) @ (posedge clk);
Boolean layer
Temporal layer
Verification layer
Modeling layer
A clock expression determining when the expression is evaluated
Identifier. If present,
it has to be unique

## Slide 7: Boolean layer

## Slide 8: (Boolean_)Expression
Expression:
  var_name (the sampled value of the variable named var_name)
  HDL expression
Boolean_Expression
  1 is True
  0,x,z is False
  e (!e) (e is an Expression having value 1, 0, x, z)
  conjunction: e1 && e2 (e1 and e2 Boolean_Expression)
  disjunction: e1 || e2 (e1 and e2 Boolean_Expression)
  implication: e1 -> e2 ( maps to (!e1 || e2) )
  equality: e1 == e2 ( maps to (e1 && e2) || (!e1 && !e2) )
  …

## Slide 9: Built-in functions
prev(expr, [i]): gives the value of expr in the ith previous cycle with respect to the clock of its context. The value of i is 1 when not specified.
  Examples:
  prev(a) gives 1 at times 5 and 7 (clk context)
  prev(a,2) gives 1 at time 7 (clk context)
time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
clk | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
a | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
Notes: No clk, returns the value 1 at times 3, 4, and 6, and the
value 0 at other times

## Slide 10: Built-in functions
next(expr): gives the value of expr at the next cycle with respect to the finest granularity of time.
  Example:
  next(a) gives 1 at times 1, 2 and 4
time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
clk | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
a | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0

## Slide 11: Built-in functions
rose(expr): takes a Bit expression as argument, and it returns True if the expr’s value is 1 at the current cycle and 0 at the previous cycle, with respect to the clock of its context.
  Example:
  rose(a) gives True at time 3 (clk context)
time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
clk | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
a | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
Notes: No clk, rose(a) is true at times 2 and 5 and at no other time,

## Slide 12: Built-in functions
fell(expr): takes a Bit expression as argument, and it returns True if the expr’s value is 0 at the current cycle and 1 at the previous cycle, with respect to the clock of its context.
  Example:
  fell(a) gives True at time 7 (clk context)
time | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
clk | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
a | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
Notes: No clk, fell(a) is true at times 4 and 6

## Slide 13: Temporal layer

## Slide 14: Property and Sequence (part 1)
Property = Boolean_Expression | Property @ clock_expression | always Property | never Property
| eventually! Property | next[i] Property | Property until Property | Property -> Property
Sequence = … (next slides)

## Slide 15: clock_expression
A clock expression is a Boolean Expression which defines a clock context. A clock context determines the path on which a Property, Sequence, or Expression is evaluated. Example: Evaluating a formula only at the positive edge of clk. (always (req -> next ack)) @ (posedge clk);
The directive default clock defines the default clock context. Example: default clock = (posdge clk); (always (req -> next ack));

## Slide 16: Temporal operator
always: the always operator specifies that a Property or a Sequence holds at all times, starting from the present.
never: the never operator specifies that a Property or a Sequence never holds.
eventually!: The eventually! operator specifies that a Property holds at the current cycle or at some future cycle.

## Slide 17: Example
If GntA is high, then GntB is low: always (GntA -> !(GntB)) @ (posedge clk);
GntA
GntB
At the rising clk, if GntA is high, then GntB is low
clk
Implication (->)
expresses “if… then”
if
then
if
then

## Slide 18: Example
ReqA is eventually followed by GntA: always (ReqA -> eventually! GntA) @ (posedge clk);
One Grant satisfies all related ‘if-then’ requirements
clk
‘eventually’ refers to now or some future cycle
ReqA
GntA
if
then
if
then
if
then
if
then
if
then
if
then

## Slide 19: Temporal operator
next: the next family specify that a Property holds at some next cycle. Property = next! (Property) | next (Property) | next![i] (Property) | next[i] (Property)
If present, the number i indicates at which next cycle the property holds.
next! and next![i], specifies that the ith next cycle must exist!

## Slide 20: Example
GntA is never high for two successive clock cycles never (GntA && next[1](GntA)) @ (posedge clk);
GntA
GntB
clk
If GntA is high for two cycles, the assertion fails

## Slide 21: Example
If GrantA, or GrantB, is high, then Busy is high after two clocks cycles: always ((GntA || GntB) -> next![2](Busy)) @(posedge clk);
Implication (->) and ‘next’ together express multi-cycle conditional behavior
GntB
clk
GntA
Busy
if
then
if
then
if
then

## Slide 22: Temporal operator
until: the until family specify that a one Property holds until a second Property holds (terminating property). Property = Property until! (Property) | Property until!_ (Property) | Property until (Property) | Property until_ (Property)
until! and until!_ operators specify that the terminating property eventually holds (otherwise the left operand holds forever).
until_ and until!_ operators specify that that the left operand holds up to and including the cycle in which the right operand holds.

## Slide 23: Example
If GntA is high, then Busy is high after one clocks cycle, and it remains high until (inclusive) Done is high always ((GntA) -> next[1](Busy until_ Done)) @(posedge clk);
Busy
clk
GntA
Done
if
then

## Slide 24: Property and Sequence (part 2)
Property = … (see previous slides) | Sequence | Sequence |-> Property | Sequence |=> Property
SERE = Boolean_Expression | SERE ; SERE | SERE : SERE | {SERE} [@ clock_expression] | repeated_SERE
A Sequence is a SERE!

## Slide 25: Sequential Extended Regular Expression (SERE)
SEREs describe single- or multi-cycle behavior built from a series of Boolean expressions.
The concatenation operator (;) constructs a SERE that is the concatenation of two other SEREs.
Informal semantic: A;B holds on a path iff there is a future cycle n, such that A holds up to and including the nth cycle, and B holds on the path starting at the (n+1)th cycle.

## Slide 26: Sequential Extended Regular Expression (SERE)
The fusion operator (:) constructs a SERE in which two SEREs overlap by one cycle. Namely, the second starts at the cycle in which the first completes.
Informal semantic: A:B holds on a path iff there is a future cycle n, such that A holds up to and including the nth cycle, and B holds on the path starting at the nth cycle.

## Slide 27: Clocked SERE
The clock operator @ defines the clock context in a SERE.
Example: The SERE {a;b} holds from time 2 to time 3 The clocked SERE {a;b}@clk holds from time 1 to time 3
time | 0 | 1 | 2 | 3 | 4
clk | 0 | 1 | 0 | 1 | 0
a | 0 | 1 | 1 | 0 | 0
b | 0 | 0 | 0 | 1 | 0

## Slide 28: Sequence is a Property
GntA is never high for two successive clock cycles never (GntA and next[1] GntA) @ (posedge clk);
never (GntA; GntA) @ (posedge clk);
A sequence is a shorthand for a series of ‘next’s
clk
GntA
Sequence/SERE
(Property = Sequence)

## Slide 29: Sequence is a Property
(Property = Sequence |-> Sequence
| Sequence |=> Sequence)
  Suffix implication operators:
  SERE_A |-> SERE_B If SERE_A completes, SERE_B has to begin in the same cycle
  SERE_A |=> SERE_B
    If SERE_A completes, SERE_B has to begin in the next cycle

## Slide 30: Example
The right-hand side (RHS) sequence is the ‘fulfilling sequence’
The left-hand side (LHS) sequence is the ‘enabling’ sequence
  always ((ReqA and next[1] GntA) -> next (Busy and next[1] Done)) @ (posedge clk);
always ({ ReqA ; GntA } |=> { Busy ; Done } ) @ (posedge clk);
if
then
The suffix implication operator says “if LHS, then RHS”

## Slide 31: Example
  always ( { A ; B } |=> { C } ) (posedge clk);
clk
C
B
A
A
start
1
no B
cancel
1
A
start
2
{A;B}
2
C
holds
2
A
start
3
{A;B}
3
A
start
4
no C
fail
3
no B
cancel
4

## Slide 32: Consecutive repetition of SERE
The SERE consecutive repetition operator ([* ]) constructs repeated consecutive concatenation of a given SERE.
repeated_SERE = SERE [*[Count]]
| SERE [+]
Count = number | lowerBound : upperBound
Example: s[*i] i consecutive repetitions of s
s[*i:j] between i to j consecutive repetitions of s
s[*] 0 or mere consecutive repetitions of s
s[+] 1 or more consecutive repetitions of s

## Slide 33: Example
If A fell (1->0), then it remains low for 2 up to 4 clock cycles
always ({ A ; !A } |=> {!A[*1:3] ; A }) @ (posedge clk);
clk
A

## Slide 34: verification layer

## Slide 35: Verification layer
The verification layer provides directives that tell a verification tool what to do with the specified sequences and properties.
PSL_directive = [Str. identifier: ] Verification_directive
Verification_directive = assert Property [report Str]
| assume Property
| cover Sequence [report Str]
…

## Slide 36: Verification directive
assert: the assert directive instructs the verification tool to verify that a property holds. It may optionally include a character string containing a message to report when the property fails to hold.
Example: assert always (ack -> next (!ack until req)) report “A second ack occurred before the next req”;
If always (ack -> next (!ack until req)) does not hold, then the message “A second ack occurred before the next req” should be displayed.

## Slide 37: Verification directive
assume: the assume directive instructs the verification tool to constrain the verification (e.g., the behavior of the input signals) so that the given property holds.
Example: assume always (ack -> next (ack));
Instructs the verification tool to constrain the verification (e.g., the behavior of the input signals) so that the property always (ack -> next !ack) holds in the design.

## Slide 38: Verification directive
cover: the cover directive directs the verification tool to check if a certain path was covered by the verification space based on a simulation test suite or a set of given constraints. It may optionally include a character string containing a message to report when the specified sequence occurs.
Example: cover {a; b; c}
report “The sequence a, b and c was covered”;
If {a;b;c} is covered at least one time, then the message “The sequence a, b and c was covered” should be displayed.

## Slide 39: A simple example
A and/or B sends ‘Req’ to the Arbiter.
Arbiter does round-robin scheduling between A,B.
Arbiter sends ‘Gnt’ back to A or B, making it Master.
Arbiter sets “Busy” while A or B is Master.
Master sets ‘DRdy’ when Data is on the bus.
Master sets ‘Done’ in the last cycle of a grant.
‘Reset’ resets the Arbiter.
Two blocks A, B exchange data via a common bus.
Arbiter
Block A
Block B
Data
DRdy
ReqA
GntA
ReqB
GntB
Busy
Done
Reset

## Slide 40: Simple example bus protocol
clk
ReqA
GntA
ReqB
GntB
Busy
DRdy
Done
‘clk’ controls sampling;
Block A makes two requests to Arbiter;
Arbiter sends ‘GntA’ twice, making A Master;
Block B makes one request to Arbiter;
Arbiter sends ‘GntB’ once, making B Master;
Arbiter sets ‘Busy’ until after Master sets ‘Done’;
Master sets ‘DRdy’ when data is on the bus;
Master sets ‘Done’ after each transfer;
Notes: DRdy = Data Ready

## Slide 41: Some assertions to check…
default clock = posedge clk;
GntA never occurs without ReqA
  assert never (GntA and !Req A);
If A receives a Grant, then B does not.
  assert always (GntA -> !GntB);
A never receives a Grant in two successive cycles.
  assert always (GntA -> next (!GntA));
A Grant is always followed by Busy at the next clock cycle.
  assert always ((GntA or GntB) -> next (Busy));
ReqA is eventually followed by GntA.
  assert always (ReqA -> eventually! GntA);

## Slide 42: More assertions to check…
If ReqB is followed by GntB, then next is Busy, and next is Done.
  assert always (ReqB -> next (GntB -> next (Busy -> next (Done))));
  assert always ({ReqB ; GntB } |=> (Busy ; Done));
If ReqB is followed by GntB, then next is Busy until Done.
  assert always (ReqB -> next (GntB -> next (Busy until Done)));
  assert always {ReqB ; GntB } |=> (Busy[*] ; Done);
A Grant is always followed by Busy until, and overlapping with, Done
  assert always ((GntA || GntB) -> next (Busy until_ Done));
  assert always ({GntA || GntB} |=> {Busy[*]:(Busy && Done)});

## Slide 43: PSL Simple subset

## Slide 44: PSL simple subset
PSL can express properties that involve jumping back and forth the future
  In static verification jumps are always possible
  In dynamic verification time advances monotonically
The Simple Subset of PSL conforms to the notion of monotonic advancement of time
  Left to right through the property

## Slide 45: An illustrative example
(α && eventually! (β)) -> (δ)
is NOT part of the Simple Subset
α
β
δ

## Slide 46: Simple Subset Restrictions
PSL Operator | Restrictions
Not | Operand must be Boolean
Never | Operand must be Boolean or sequence
eventually! | Operand must be Boolean or sequence
or | At most one operand may be non-Boolean
-> | LHS must be Boolean or sequence
<-> | Both operands must be Boolean
until until! | RHS must be Boolean
until_ until!_ | Both operands must be Boolean